## Slide 1: “Environmental Impact Assessment of Proposed Rough Stone and Gravel Quarry – Karasanur Village, Vanur Taluk, Viluppuram District, Tamil Nadu”
Team Members :
Farzana Shereef
Febin Biju
Hanna Mariam Jiby
Helena Tom
Issac Jeevan
Jestrin K Joice
Johnson V Mathew
Submitted To
Mrs. AMRUTHA S
A.P , CED

## Slide 2: Introduction
Environmental Impact Assessment (EIA) for the proposed Rough Stone & Gravel Quarry at Karasanur, Viluppuram, Tamil Nadu.
Conducted as per EIA Notification, 2006 & amendments.
Aims to study baseline environment, assess impacts, and propose mitigation.
Essential step for obtaining Environmental Clearance (EC) and ensuring sustainable mining.

## Slide 3: Project Overview
Proposed Rough Stone & Gravel Quarry Project
Location: Karasanur Village, Vanur Taluk, Viluppuram District, Tamil Nadu
Lease area: 2.02.5 Ha; Cluster area: 9.02.5 Ha
Project Proponent: Tmt. K. Rajamani
Consultant: M/s. Global Mining Solutions (NABET Accredited)
Proposed production (5 years):
Rough Stone – 2,31,505 m³
Gravel – 33,696 m³
EIA conducted as per EIA Notification 2006 & amendments
Study carried out March–May 2024

## Slide 4: Objectives of EIA
To establish baseline environmental conditions (air, water, soil, noise, socio-economic).
To assess potential impacts of quarrying activities on the environment and community.
To propose mitigation and management measures for minimizing adverse effects.
To develop an Environmental Management Plan (EMP) for sustainable quarry operations

## Slide 5: Baseline Environmental Conditions
Study Area – 10 km radius around the quarry; survey conducted March–May 2024.
Air Quality – PM₂.₅, PM₁₀, SO₂, NOx monitored at 6 locations; values compared with NAAQS standards.
Water Quality – Surface & ground water samples analyzed for physical, chemical, and biological parameters.
Noise & Vibration – Baseline noise: 52–72 dB(A) (day), 40–65 dB(A) (night); vibration assessed for blasting safety.

## Slide 6: Environmental Management Plan (EMP)
Air Pollution Control – Wet drilling, controlled blasting, water sprinkling, greenbelt (1300 saplings).
Water & Waste Management – Stormwater drainage, reuse of quarry pit water, proper disposal of solid & domestic waste.
Noise & Vibration Control – Controlled blasting, maintenance of machinery, use of PPE for workers.
Socio-Economic Measures – Employment generation, CSR activities, health & safety training for workers.

## Slide 7: Risk Assessment and Disaster Management
Controlled Blasting & Safety – Use of line drilling, controlled blasting, protective gear, and trained supervisors to reduce vibration, dust, and accident risks.
Risk Identification – Monitoring slope stability, dust exposure, and equipment handling hazards.
Emergency Response – Prepared ERP with clear staff roles, firefighting measures, and evacuation plan.
Health & Disaster Preparedness – First-aid/medical support, tie-up with hospitals, and cluster-level planning for floods, heavy rains, and other calamities.

## Slide 8: Project Benefits
Infrastructure Development – Improves local roads, transport facilities, and availability of construction materials.
Employment Generation – Creates direct and indirect jobs for skilled, semi-skilled, and unskilled workers.
Socio-Economic Growth – Boosts income opportunities for nearby villages and supports local businesses.
Community Support & Greenbelt – Funds for CSR/CER activities, plantation, and environmental protection measures.

## Slide 9: Conclusion
The project is planned with scientific mining methods ensuring safety and sustainability.
Anticipated environmental impacts are minor and will be mitigated with proper measures.
Implementation of EMP, greenbelt, and monitoring programs will protect the local environment.
The project will bring economic, social, and infrastructure benefits to the region.

## Slide 10: References
Draft EIA/EMP Report for the Proposed Rough Stone and Gravel Quarry at Karasanur Village, Vanur Taluk, Viluppuram District, Tamil Nadu. Prepared by M/s. Global Mining Solutions, August 2024.

## Slide 11: THANK YOU