## Slide 1: Environmental Impact Assessment Umngot Hydroelectric Project (210 MW)
TEAM MEMBERS:
Alwin Lal
Aman Besty
Anirudh K B
Anjana Jomon
Ann Merin Shaji
Ansel Sajan
Aswin Jim Thuruthippilly
SUBMITTED TO:
Amrutha S
A.P, CED

## Slide 2: Introduction
India’s hydropower potential is 148,700 MW, with only 30.6% harnessed.
The Northeast region holds 58,956 MW, but Meghalaya has low installed capacity (387.19 MW).
The Umngot HEP (210 MW) addresses regional power shortages, with 708.98 MU annual generation.

## Slide 3: Project Description
The Umngot HEP is a storage scheme on Umngot River.
It involves a 111 m high concrete gravity dam, 71.31 MCM reservoir, 5.646 km tunnel, and 3 Pelton turbines (70 MW each).
Land requirement is 390.5 ha, with 6 years construction and cost Rs. 2,567.80 Cr.

## Slide 4: Baseline Environment (Physical and Chemical)
Topography: Shillong Plateau, altitudes 150–1965 m.
Geology: granite gneiss, Zone V seismicity.
Land use: dense forest 34%, open forest 24%.
Climate: tropical monsoon, avg rainfall 2250 mm.
Air & noise within limits except construction sites.
Soil: sandy loam, fertile but nutrient-limited.
Water: clean, Class A quality.

## Slide 5: Baseline Environment (Biological and Socio-Economic)
Flora: 135 species, no rare/endangered.
Fauna: 47 mammals, 137 birds, 28 reptiles. Aquatic biodiversity low.
Population in project-affected villages: 149 (Khasi tribe), literacy 80–90%.
Economy: agriculture-based, limited infrastructure.
157 families affected by land acquisition.

## Slide 6: Anticipated Environmental Impacts and Mitigation Measures
Impacts: forest loss (93.53 ha), displacement (157 families), turbidity, dust, noise, muck disposal.
Mitigation: Compensatory afforestation, sewage treatment, water sprinkling, controlled blasting, CAT plan, fisheries plan, muck disposal sites.

## Slide 7: Anticipated Environmental Impacts and Mitigation Measures
Socio-economic impacts: labor influx, health risks, traffic, cultural change.
Mitigation: labor camps with sanitation, health care, 80% local employment.
Operation impacts: reduced downstream flow mitigated by e-flow release.
Alternatives studied: tunneling, site options.

## Slide 8: Alternative Analysis and 'No Project Scenario'
No Project Scenario: Power shortages in NE India persist.
With Project: 210 MW peaking power, employment, tourism, improved livelihoods, reduced migration.
Alternatives: original submergence (320 ha) vs final (253.75 ha), drill-blast chosen over TBM due to geology.

## Slide 9: Environmental Management Plan - Air & Noise
Measures: water sprinkling for dust, green belt development, mufflers for equipment, blasting control, noise monitoring, PPE for workers.
Reservoir rim stabilization, quarry rehabilitation included.

## Slide 10: EMP - Water, Land and Biodiversity
Measures: STP for sewage, e-flow release, muck disposal sites, CAT plan (222 ha treated), compensatory afforestation (187 ha), biodiversity management, fisheries hatchery and stocking, green belt along reservoir.

## Slide 11: Environmental Monitoring Plan
Air, water, soil, noise monitored quarterly.
E-flow, aquatic ecology, biodiversity checked. Monitoring cost Rs. 2.01 Cr.
Remote sensing used. EMP implementation reviewed regularly with adaptive measures.

## Slide 12: Environmental Monitoring Plan
Construction and operation phases both covered.
Reports prepared quarterly.
Independent monitoring by accredited labs.
Focus on compliance with CPCB/IS standards.
Costs integrated into EMP budget (Rs. 36.3 Cr).

## Slide 13: Conclusion
The Umngot HEP (210 MW) provides renewable power with minimal footprint.
With strict EMP, displacement, habitat loss, and pollution are mitigated.
Benefits: clean energy, jobs, economic growth, tourism.
Project is viable and sustainable with community participation.