## Slide 1
CST303-Computer Networks

## Slide 2
Text Books
1. Andrew S. Tanenbaum, Computer Networks, 4/e, PHI (Prentice Hall India).
2. Behrouz A Forouzan, Data Communication and Networking, 4/e, Tata McGraw Hill
Reference Books
1.Larry L Peterson and Bruce S Dave, Computer Networks – A Systems Approach, 5/e, Morgan Kaufmann.
2.Fred Halsall, Computer Networking and the Internet, 5/e.
3.James F. Kurose, Keith W. Ross, Computer Networking: A Top-Down Approach, 6/e.
4.Keshav, An Engineering Approach to Computer Networks, Addison Wesley, 1998.
5.W. Richard Stevens. TCP/IP Illustrated Volume 1, Addison-Wesley, 2005.
6.William Stallings, Computer Networking with Internet Protocols, Prentice-Hall, 2004.
7.Request for Comments (RFC) Pages - IETF -https://www.ietf.org/rfc.html

## Slide 3: Syllabus
Module I
Introduction – Uses of computer networks, Network hardware, Network software. Reference models – The OSI reference model, The TCP/IP reference model, Comparison of OSI and TCP/IP reference models.
Physical Layer – Modes of communication, Physical topologies, Signal encoding, Repeaters and hub, Transmission media overview. Performance indicators – Bandwidth, Throughput, Latency, Queuing time, Bandwidth–Delay product.

## Slide 4: Introduction
Computer Network:
A network can be defined as a group of computers and other devices connected in some way so as to be able to exchange data.
  Communication is the process of exchanging information between two persons or devices
  Connection can be made via copper wire, fiber optics, microwaves or communication satellites etc
  If one computer cannot forcibly start, stop or control another computer then it is termed as autonomous

## Slide 5: USES OF COMPUTER NETWORKS

## Slide 6: Uses of Computer Networks
  Business Applications or Networks for companies
  Home applications or Networks for People
  Mobile Network Users
  Social Issues

## Slide 7: USES OF COMPUTER NETWORKS
Business Applications
Resource sharing - to make all programs, equipment, and especially data available to anyone on the network without regard to the physical location of the resource or the user
  Eg: a group of office workers sharing a common printer
Sharing information - Most companies have customer records, product information, inventories, financial statements, tax information, and much more online
  VPNs (Virtual Private Networks) may be used to join the individual networks at different sites into one extended network

## Slide 8: Business Applications
Client-server model
Data are stored on powerful computers called servers. Often these are centrally housed and maintained by a system administrator.
Employees have simpler machines, called clients, with which they access remote data, for example, to include in spreadsheets they are constructing.
Most popular realization - Web application
One server can handle a large number (hundreds or thousands) of clients simultaneously.

## Slide 9: Business Applications
Client-server model
Communication takes the form of the client process sending a message over the network to the server process.
The client process then waits for a reply message.
When the server process gets the request, it performs the requested work or looks up the requested data and sends back a reply.

## Slide 10: Business Applications
email (electronic mail)
Provide a powerful communication medium among employees
IP telephony or Voice over IP (VoIP)
The microphone and speaker at each end may belong to a VoIP-enabled phone or the employee’s computer.
Companies find this a wonderful way to save on their telephone bills.
Desktop sharing
Lets remote workers see and interact with a graphical computer screen.
This makes it easy for two or more people who work far apart to read and write a shared blackboard or write a report together

## Slide 11: Home Network Applications
Access to remote information
  Home shopping
  Online newspaper
  Access to WWW
Person-to-person communication
  E-mails
  Video conference
  Worldwide newsgroup

## Slide 12: Home Network Applications
Interactive entertainment
  Video on demand
  Live Television
  Game playing
Electronic commerce (e-commerce)
  convenience of shopping from home with online catalogs

## Slide 13: Home Network Applications
In peer-to-peer system there are no fixed clients and servers.

## Slide 14: Mobile Network Users
Mobile commerce (m-commerce)-Short text messages from the mobile are used to authorize payments for food in vending machines, movie tickets, and other small items instead of cash and credit cards.
Wearable computers
Smart watches with radio.
Implanted devices
Pacemakers and insulin pumps.
Some of these can be controlled over a wireless network

## Slide 15
Mobile Network Users
Combinations of wireless networks and mobile computing.

## Slide 16: Social Issues
Social networks, message boards, content sharing sites, and a host of other applications allow people to share their views with like-minded individuals.
Exchange messages using newsgroup may lead to conflicts.
Employee rights vs employer rights
Network offers the potential to send anonymous messages
Electronic junk mails (Spam) may contain viruses
Another conflict is centered around government versus citizen’s rights. The FBI has installed systems at many Internet service providers to snoop on all incoming and outgoing email.

## Slide 17: Social Issues
Companies that provide Web-based services may maintain large amounts of personal information about their users that allows them to study user activities directly.
For example, Google can read your email and show you advertisements based on your interests if you use its email service, Gmail.
Phishing messages looks as originating from a trustworthy party, for example, your bank, to try to trick you into revealing sensitive information, for example, credit card numbers.
Identity theft is becoming a serious problem as thieves collect enough information about a victim to obtain credit cards and other documents in the victim’s name.
A lot of these problems could be solved if the computer industry took computer security seriously.
If all messages were encrypted and authenticated, it would be harder to commit mischief.

## Slide 18: NETWORK HARDWARE

## Slide 19
Based on types of transmission technology
  Broadcast Networks
  Point-to-point Networks
Based on Scale
Network Hardware

## Slide 20
Broadcast Networks
  A single communication channel is shared by all the machines on the network
  Short messages called packets sent by any machine are received by all the others
  Address field in a packet specifies the recipient
  After receiving the packet, the address field is checked
  If it is intended for itself, it processes the packet, otherwise it is ignored
Network Hardware

## Slide 21
Broadcasting
  Broadcast systems allow the possibility of addressing a packet to all destinations by using special code in the address field
  Smaller localized network use broadcasting
Multicasting
  Broadcast systems also support transmission to a subset of the machines
  By reserving a bit to indicate multicasting & the remaining n-1 address bits can hold the group number
  Each machine can subscribe to any or one of the groups
Network Hardware

## Slide 22
Point-to-point Networks
  Many connections between individual pair of machines
  Transfer from source to destination may includes one or more intermediate machines
  Multiple routes of different lengths leads to the role of routing algorithm for route selection
  Larger networks use point-to-point
  Point-to-point transmission with one sender and one receiver is sometimes called unicasting
Network Hardware

## Slide 23: Point-to-point links

## Slide 24: Network Hardware
Based on Scale
  Personal Area Networks
  Local Area Networks
  Metropolitan Area Networks
  Wide Area Networks
  Internetworks or Internet

## Slide 25: Network Hardware
Personal Area Networks
  Networks that are meant for one person
  Eg: a wireless network connecting a computer with its mouse, keyboard, and printer
Local Area Networks
  Generally called as LANs
  Privately owned networks
  Inter-processor distance:10m to 1km
  Networks placed in a single room or building or campus
  LANs are distinguished by 3 characteristics –
    Size
    Transmission Technology
    Topology

## Slide 26: LAN
  Size :-
  Worst-case transmission time is bounded and known in advance.
  Knowing this bound makes it possible to use certain kinds of designs
  Simplifies Network management.
Transmission Technology :-
  consist of a single cable to which all the machines are attached .
  Traditional LAN runs at speed of 10 to 100 Mbps
  Newer LANs operate at 10 Gbps
  Low delay
  Makes very few errors

## Slide 27: LAN
Topology :-
2 broadcast network types:
    Bus & Ring
  Bus (Linear cable) network
    at any instant, at most one machine is the master and is allowed to transmit.
    All other machines are required to refrain from sending
    Arbitration mechanism :- to resolve conflicts when two or more machines want to transmit simultaneously.
    It may be Centralized or distributed (decentralized)

## Slide 28: LAN
Eg:-IEEE 802.3 popularly called Ethernet is bus based broadcast network with decentralized control
  operates at 10 Mbps to 10 Gbps
  Computers on an Ethernet can transmit whenever they want to;
  if two or more packets collide, each computer just waits a random time and tries again later

## Slide 29: LAN
Ring Network:
  Devices acts as repeaters to boost the signal
  The transmission of data takes place by token passing.
  A token is a special series of bits that contains control information.
  Possession of the token allows a network device to transmit data to the network.
  Each network has only one token.

## Slide 30: LAN
Working of Ring Network:
  The sending computer removes the token from the ring and sends the requested data around the ring.
  Each computer passes the data until the packet finds the computer that matches the address on the data.
  The receiving computer then returns a message to the sending computer indicating that the data has been received.
  After verification, the sending computer creates a new token and releases it to the network.

## Slide 32: LAN
Ring Network:
Advantages:
Very orderly network where every device has access to the token and the opportunity to transmit
Performs better than a bus topology under heavy network load
Does not require network server to manage the connectivity between the computers
Disadvantages:
One malfunctioning workstation or bad port can create problems for the entire network
Devices moved, added and changed can affect the network
Network adapter cards are much more expensive than Ethernet cards and hubs
Much slower than an Ethernet network under normal load

## Slide 33: LAN
Ring Network:
  Egs:
    IEEE 802.5 (the IBM token ring), is a ring-based LAN
      operates at 4 and 16 Mbps.
    FDDI (Fiber Distributed Data Interface) is another example of a ring network

## Slide 34: LAN
Broadcast networks can be further divided into 2, depending on how the channel is allocated
  Static and Dynamic
A typical static allocation is
  to divide time into discrete intervals and use a round-robin algorithm
  allowing each machine to broadcast only when its time slot comes up
  Drawback: wastes channel capacity when a machine has nothing to say during its allocated slot
  So, most systems attempt to allocate the channel dynamically (i.e., on demand).

## Slide 35: LAN
Dynamic allocation methods are either centralized or decentralized.
In the centralized channel allocation method,
  there is a single entity,
  for example, a bus arbitration unit,
  which determines who goes next.
  It might do this by accepting requests and making a decision according to some internal algorithm.
In the decentralized channel allocation method,
  there is no central entity;
  each machine must decide for itself whether to transmit.

## Slide 36: Metropolitan Area Networks (MAN)
A metropolitan area network based on cable TV in a city.
Another eg: IEEE 802.16 (Broadband wireless MANs) for high-speed wireless Internet access

## Slide 37: Wide Area Networks (WAN)
WAN spans a large geographical area, often a country or continent
It contains a collection of machines called hosts intended for running user (i.e., application) programs
The hosts are owned by the customers
The hosts are connected by a communication subnet, or just subnet
The communication subnet is typically owned and operated by a telephone company or Internet service provider
The job of the subnet is to carry messages from host to host, just as the telephone system carries words from speaker to listener

## Slide 38: Wide Area Networks (WAN)
Subnet consists of two distinct components:
  transmission lines
  switching elements
Transmission lines
  move bits between machines.
  made of copper wire, optical fiber, or even radio links.
Switching elements
  Specialized computers that connect three or more transmission lines.
  When data arrive on an incoming line, it must choose an outgoing line on which to forward them.
  Switching elements are also called as routers

## Slide 39: Wide Area Networks (WAN)
Relation between hosts on LANs and the subnet.

## Slide 40: Wide Area Networks (WAN)
Store-and-forward or packet-switched subnet
  When a packet is sent from one router to another via one or more intermediate routers,
  the packet is received at each intermediate router in its entirety,
  stored there until the required output line is free, and then forwarded.
  When the packets are small and all of the same size, they are often called cells

## Slide 41: Wide Area Networks (WAN)
Principle of a packet-switched WAN:
  When a process on some host has a message to be sent to a process on some other host,
  the sending host first cuts the message into packets,
  each one bearing its number in the sequence.
  These packets are then injected into the network one at a time in quick succession.
  The packets are transported individually over the network and deposited at the receiving host,
  where they are reassembled into the original message and delivered to the receiving process

## Slide 42: Wide Area Networks
A stream of packets from sender to receiver.
Routing decisions are made locally.
When a packet arrives at router A, it is up to A to decide if this packet should be sent on the line to B or the line to C.
How A makes that decision is called the routing algorithm.

## Slide 43: Wide Area Networks (WAN)
Not all WANs are packet switched.
A second possibility for a WAN is a satellite system.
Each router has an antenna through which it can send and receive.
All routers can hear the output from the satellite
In some cases, they can also hear the upward transmissions of their fellow routers to the satellite as well.
Sometimes the routers are connected to a substantial point-to-point subnet, with only some of them having a satellite antenna.
Satellite networks are inherently broadcast and are most useful when the broadcast property is important

## Slide 44: Internetworks
A collection of interconnected networks is called an internetwork or internet
A common form of internet is a collection of LANs connected by a WAN
If the intermediate system contains only routers, it is a subnet
if it contains both routers and hosts, it is a WAN
An internetwork is formed when distinct networks are interconnected

## Slide 45: Network Software
Protocol Hierarchies
Design Issues for the Layers
Connection-Oriented and Connectionless Services
Service Primitives
The Relationship of Services to Protocols

## Slide 46: Protocol Hierarchies
To reduce their design complexity, most networks are organized as a stack of layers or levels
Number of layers, name of each layer, contents of each layer, and function of each layer differ from network to network
Purpose of each layer
  to offer certain services to the higher layers,
  shielding those layers from the details of how the offered services are actually implemented
The rules and conventions used in this conversation are collectively known as the layer n protocol
Protocol is an agreement between the communicating parties on how communication is to proceed

## Slide 47: Network Software Protocol Hierarchies

## Slide 48: Protocol Hierarchies
No data are directly transferred from layer n on one machine to layer n on another machine.
Instead, each layer passes data and control information to the layer immediately below it, until the lowest layer is reached.
Below layer 1 is the physical medium through which actual communication occurs
Between each pair of adjacent layers is an interface
Interface defines which primitive operations and services the lower layer makes available to the upper one

## Slide 49: Protocol Hierarchies
Clear-cut interfaces makes it simpler to replace the implementation of one layer with a completely different implementation
e.g., all the telephone lines are replaced by satellite channels
A set of layers and protocols is called a network architecture
A list of protocols used by a certain system, one protocol per layer, is called a protocol stack

## Slide 50: Protocol Hierarchies

## Slide 51: Protocol Hierarchies
header & trailer includes control information, such as sequence numbers, sizes, times, and other control fields

## Slide 52: Design Issues for the Layers
Addressing
Rules for data transfer
Error Control
Flow Control
Long messages
Too short messages
Multiplexing & demultiplexing
Routing

## Slide 53: Design Issues for the Layers
Addressing
  Every layer needs a mechanism for identifying senders and receivers
  So, addressing is required
Rules for data transfer
  Unidirectional or bidirectional (Simplex / Half duplex / Full duplex)
  Protocol must determine how many logical channels the connection corresponds to and what their priorities are
  Many networks provide at least two logical channels per connection, one for normal data and one for urgent data.

## Slide 54: Design Issues for the Layers
Error Control
  Problem: physical communication circuits are not perfect
  error-detecting and error-correcting codes are available
  both ends of the connection must agree on which one is being used
  receiver must have some way of telling the sender which messages have been correctly received and which have not
  To deal with a possible loss of sequencing, the protocol must make explicit provision for the receiver to allow the pieces to be reassembled properly

## Slide 55: Design Issues for the Layers
Flow Control
  Problem: how to keep a fast sender from swamping (overloading) a slow receiver with data
  Solution 1: some kind of feedback from the receiver to the sender, about the receiver's current situation
  Solution 2: limit the sender to an agreed-on transmission rate (flow control)
Long messages
  Problem: inability of all processes to accept arbitrarily long messages
  Solution: disassembling, transmitting, and then reassembling messages

## Slide 56: Design Issues for the Layers
Too short messages
  Problem: transmitting data in units that are so small that sending each one separately is inefficient.
  Solution: to gather several small messages heading toward a common destination into a single large message and dismember the large message at the other side.
Multiplexing & demultiplexing
  underlying layer may decide to use the same connection for multiple, unrelated conversations (Physical layer)
Routing
  When there are multiple paths between source and destination, a route must be chosen based on the current traffic load

## Slide 57: Connection-Oriented Services
Similar to telephone service
to use a connection-oriented network service, the service user
  establishes a connection,
  uses the connection, and
  releases the connection
acts like a tube
  sender pushes objects (bits) in at one end, and the receiver takes them out at the other end
  the order is preserved so that the bits arrive in the order they were sent

## Slide 58: Connection-Oriented Services
When a connection is established, the sender, receiver, and subnet conduct a negotiation
about parameters to be used, such as
  maximum message size,
  quality of service
    error rates,
    bandwidth,
    throughput,
    transmission delay,
    jitter,
    Availability
  other issues.
Typically, one side makes a proposal and the other side can accept it, reject it, or make a counterproposal

## Slide 59: Connection-Oriented Services
Classifications: Reliable & Unreliable
Each service can be characterized by a quality of service
Some services are reliable that they never lose data.
A reliable service is implemented by having the receiver acknowledge the receipt of each message so the sender is sure that it arrived.
The acknowledgement process introduces overhead and delays, which are often worth it but are sometimes undesirable
Eg for reliable connection-oriented service is file transfer
Reliable connection-oriented service has two minor variations:
  message sequences and
  byte streams

## Slide 60: Connection-Oriented Services
Message sequences
  message boundaries are preserved.
  When two 1024-byte messages are sent, they arrive as two distinct 1024-byte messages, never as one 2048-byte message
  Eg: Sending the pages of book
Byte streams
  connection is simply a stream of bytes, with no message boundaries.
  When 2048 bytes arrive at the receiver, there is no way to tell if they were sent as one 2048-byte message, two 1024-byte messages, or 2048 1-byte messages
  Eg: user logging details to a remote server

## Slide 61: Connection-Oriented Services
For some applications, transit delays introduced by acknowledgements are unacceptable. (Unreliable is better)
Application 1: digitized voice traffic.
  It is preferable for telephone users to hear a bit of noise on the line from time to time than to experience a delay waiting for acknowledgements.
Application 2: video conference
  when transmitting a video conference, having a few pixels wrong is no problem, but having the image jerk along as the flow stops to correct errors is irritating

## Slide 62: Connectionless Services
Similar to postal system
Each message (letter) carries the full destination address
Each one is routed through the system independent of all the others

## Slide 63: Connectionless Services
Connectionless service is often called datagram service
Unreliable (meaning not acknowledged) datagram service
  does not return an acknowledgement to the sender
  Eg: junk mails
acknowledged datagram service
  convenience of not having to establish a connection to send one short message is desired,
  but reliability is essential.
  Eg: sending a registered letter and requesting a return receipt
request-reply service
  the sender transmits a single datagram containing a request; the reply contains the answer
    Egs: a query to the local library, Client server model

## Slide 64: Connection-Oriented and Connectionless Services
Six different types of service.

## Slide 65: Interfaces & Services
Active elements in each layer are called entities
An entity can be a
  software entity (such as a process), or
  hardware entity (such as an intelligent I/O chip)
Entities in the same layer on different machines are called peer entities
Entities in layer n implement a service used by layer n+ 1
  Layer n is the service provider
  Layer n + 1 is the service user
Classes of services
  Fast & expensive communication
  Slow & cheap communication

## Slide 66: Service Primitives
A service is specified by a set of primitives (operations) available to a user process to access the service.
These primitives tell the service to perform some action or report on an action taken by a peer entity.
If the protocol stack is located in the operating system, the primitives are normally system calls.
These calls cause a trap to kernel mode, which then turns control of the machine over to the operating system to send the necessary packets.

## Slide 67: Service Primitives
Five service primitives for implementing a simple connection-oriented service.

## Slide 68: Service Primitives
Packets sent in a simple client-server interaction on a connection-oriented network.

## Slide 69: Service Primitives
Eg Illustration:
Server executes LISTEN to indicate that it is prepared to accept incoming connections.
A common way to implement LISTEN is to make it a blocking system call.
After executing the primitive, the server process is blocked until a request for connection appears
Client process executes CONNECT to establish a connection with the server
Operating system then typically sends a packet to the peer asking it to connect
Client process is suspended until there is a response

## Slide 70: Service Primitives
When the packet arrives at the server, it is processed by its operating system
When the system sees that the packet is requesting a connection, it checks to see if there is a listener.
If so, it does two things:
  unblocks the listener and
  sends back an acknowledgement
arrival of this acknowledgement then releases the Client
At this point the Client and Server are both running and they have a connection established
If a connection request arrives and there is no listener, the result is undefined

## Slide 71: Service Primitives
The next step is for the Server to execute RECEIVE to prepare to accept the first request.
  Normally, the server does this immediately upon being released from the LISTEN, before the acknowledgement can get back to the client.
The RECEIVE call blocks the Server
Then the Client executes SEND to transmit its request followed by the execution of RECEIVE to get the reply
The arrival of the request packet at the server machine unblocks the Server process so it can process the request.
After it has done the work, it uses SEND to return the answer to the Client.
The arrival of this packet unblocks the Client, which can now inspect the answer.

## Slide 72: Service Primitives
If the Client has additional requests, it can make them now.
If it is done, it can use DISCONNECT to terminate the connection.
Usually, an initial DISCONNECT is a blocking call, suspending the client and sending a packet to the server saying that the connection is no longer needed.
When the Server gets the packet, it also issues a DISCONNECT of its own, acknowledging the client and releasing the connection.
When the Server's packet gets back to the Client machine, the Client process is released and the connection is broken.

## Slide 73: Reference Models
The OSI Reference Model
The TCP/IP Reference Model

## Slide 74: OSI Reference Model
The model is called the ISO OSI (International Organization for Standardization Open Systems Interconnection) Reference Model.
because it deals with connecting open systems
  ie, systems that are open for communication with other systems
OSI model has seven layers
      Physical layer
      Data link layer
      Network Layer
      Transport Layer
      Session Layer
      Presentation Layer
      Application Layer

## Slide 75: OSI Reference Model
Principles behind the seven layer design
  A layer should be created where a different abstraction (concept) is needed.
  Each layer should perform a well-defined function.
  The function of each layer should be based on internationally Standardized Protocols
  The layer boundaries should be chosen to minimize the information flow across the interfaces
  Number of layers should be
    large enough that distinct functions need not be thrown together in the same layer out of necessity
    small enough that the architecture does not become unmanageable

## Slide 76: OSI Reference Models

## Slide 77: Organization of the Layers
The seven layers can be thought of as belonging to three subgroups.
Layers I, 2, and 3-physical, data link, and network-are the network support layers
They deal with the physical aspects of moving data from one device to another (such as electrical specifications, physical connections, physical addressing, and transport timing and reliability).
Layers 5, 6, and 7-session, presentation, and application-can be thought of as the user support layers
They allow interoperability among unrelated software systems.
Layer 4, the transport layer, links the two subgroups and ensures that what the lower layers have transmitted is in a form that the upper layers can use.
The upper OSI layers are almost always implemented in software
Lower layers are a combination of hardware and software, except for the physical layer, which is mostly hardware.

## Slide 78: Figure: An exchange using the OSI model

## Slide 79: OSI Reference Model
Physical Layer
The physical layer has as a main function to transmit bits over a communication channel as well as to establish and terminate a connection to a communications medium.
  concerned with transmitting raw bits over a communication channel
  Design issues are
    when one side sends a 1 bit, it is received by the other side as a 1 bit, not as a 0 bit.
    how many volts should be used to represent a 1 and how many for a 0,
    how many nanoseconds a bit lasts,
    whether transmission may proceed simultaneously in both directions,
    how the initial connection is established and
    how it is torn down when both sides are finished,
    how many pins the network connector has
    what each pin is used for

## Slide 80
Figure : Physical layer

## Slide 81: OSI Reference Model
Physical Layer
  Design issues deal with
    Mechanical, electrical, & timing interfaces, and physical transmission medium, which lies below the physical layer
Data link Layer
  Main task: Error Control
    The data link layer transforms the physical layer, a raw transmission facility, to a reliable link.
    It makes the physical layer appear error-free to the upper layer (network layer).
    If the service is reliable, the receiver confirms correct receipt of each frame by sending back an acknowledgement frame
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.

## Slide 82
Framing-The data link layer divides the stream of bits received from the network layer into manageable data units called frames.
Physical addressing- If frames are to be distributed to different systems on the network, the data link layer adds a header to the frame to define the sender and/or receiver of the frame. If the frame is intended for a system outside the sender's network, the receiver address is the address of the device that connects the network to the next one.
Flow control- If the rate at which the data are absorbed by the receiver is less than the rate at which data are produced in the sender, the data link layer imposes a flow control mechanism to avoid overwhelming the receiver.

## Slide 83: OSI Reference Model
Error control-The data link layer adds reliability to the physical layer by adding mechanisms to detect and retransmit damaged or lost frames. It also uses a mechanism to recognize duplicate frames. Error control is normally achieved through a trailer added to the end of the frame.
Access control. When two or more devices are connected to the same link, data link layer protocols are necessary to determine which device has control over the link at any given time.
  Data link layer is subdivided into 2 for this purpose
    Logical Link Control (LLC) sub layer
    Medium Access Control (MAC) sub layer
      MAC handles the broadcast networks
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 84: OSI Reference Model
Network Layer
  The network layer is responsible for the source-to-destination delivery of a packet, possibly across multiple networks (links).
  Controls the operation of the subnet.
  Design issues
    Determining how packets are routed from source to destination
    Routes
      can be based on static tables that are fixed into the network and are rarely changed
      can be highly dynamic, being determined anew for each packet, to reflect the current network load
      can also be determined at the start of each conversation (e.g., a login to a remote machine)

## Slide 85: OSI Reference Model
Network Layer
  Congestion control
    If too many packets are present in the subnet at the same time, they will get in one another's way creating congestion
  3. Providing QOS
    transit time, delay, jitter, error rate, bandwidth, availability, throughput, etc
  4. Interconnect heterogeneous networks
    The addressing used by the second network may be different from that used by the first one.
    The second one may not accept the packet at all because it is too large.The protocols may differ
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.

## Slide 86
Figure :- Source-to-destination delivery

## Slide 87: OSI Reference Model
Transport Layer
The transport layer is responsible for process-to-process delivery of the entire message.
  Basic function
    to accept data from above,
    split it up into smaller units if needed,
    pass these to the network layer, and
    ensure that all the pieces arrive correctly at the other end.
    All this must be done efficiently in a way that isolates the upper layers from the inevitable changes in the hardware technology
    determines what type of service to provide to the session layer, and, ultimately, to the users of the network

## Slide 88: OSI Reference Model
Transport Layer
  most popular type of transport connection
    error-free point-to-point channel that delivers messages or bytes in the order in which they were sent
  other possible kinds of transport service
    transporting of isolated messages, with no guarantee about the order of delivery,
    broadcasting of messages to multiple destinations
  Type of service is determined when the connection is established

## Slide 89: OSI Reference Model
Transport Layer
  transport layer is a true end-to-end layer, all the way from the source to the destination
  ie, a program on the source machine carries on a conversation with a similar program on the destination machine, using the message headers and control messages.
  In the lower layers, the protocols are between each machine and its immediate neighbors (routers), and not between the ultimate source and destination machines
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 90
Figure :- Reliable process-to-process delivery of a message

## Slide 91: OSI Reference Model
Session Layer
  allows users on different machines to establish sessions between them
  Sessions offer various services, including
    Dialog control
      keeping track of whose turn it is to transmit
    Token management
      preventing two parties from attempting the same critical operation at the same time
    Synchronization
      check pointing long transmissions to allow them to continue from where they were after a crash
The session layer is responsible for dialog control and synchronization.

## Slide 92: OSI Reference Model
Presentation Layer
  Concerned with the syntax and semantics of the information transmitted
  Translation- The presentation layer at the sender changes the information from its sender-dependent format into a common format. The presentation layer at the receiving machine changes the common format into its receiver-dependent format.
  Encryption- To carry sensitive information, a system must be able to ensure privacy. Encryption means that the sender transforms the original information to another form and sends the resulting message out over the network. Decryption reverses the original process to transform the message back to its original form.

## Slide 93
Compression-Data compression reduces the number of bits contained in the information. Data compression becomes particularly important in the transmission of multimedia such as text, audio, and video.
The presentation layer is responsible for translation, compression, and encryption.

## Slide 94: OSI Reference Model
Application Layer
  Contains a variety of protocols that are commonly needed by users
  Widely-used application protocol
    HTTP (Hyper Text Transfer Protocol)
      basis for the World Wide Web
      When a browser wants a Web page, it sends the name of the page it wants to server using HTTP
      server then sends the page back
  Other application protocols
      File transfer (FTP)
      Electronic mail (SMTP)
      Domain Name System (DNS)
      Network News Transfer Protocol (NNTP)

## Slide 95
The application layer is responsible for providing services to the user.

## Slide 96
Figure :- Summary of layers

## Slide 97: TCP/IP Reference Models

## Slide 98: TCP/IP Reference Model
Reference model used in the ARPANET (grandparent of all WAN) and its successor, the worldwide Internet
ARPANET (Advanced Research Projects Agency Network)
  Research network sponsored by the DoD (U.S. Department of Defense)
  Connected hundreds of Universities and Government installations, using leased telephone lines
  When satellite and radio networks were added later, the existing protocols had trouble interworking with them
  So, a new reference architecture was needed
  Thus, the ability to connect multiple networks in a seamless way was one of the major design goals from the very beginning
  This architecture later became known as the TCP/IP Reference Model, after its two primary protocols

## Slide 99: TCP/IP Reference Model
Another major goal
  network must be able to survive loss of subnet hardware, with existing conversations not being broken off.
  ie, DoD wanted connections to remain intact as long as the source and destination machines were functioning
    even if some of the machines or transmission lines in between were suddenly put out of operation.
  Also, a flexible architecture was needed
    since applications with divergent requirements were envisioned, ranging from transferring files to real-time speech transmission

## Slide 100: TCP/IP Reference Model
Host-to-Network Layer
  host has to connect to the network using some protocol so that it can send IP packets to it
  protocol is not defined and varies from host to host and network to network
  TCP/IP reference model does not really say much about what happens here
Internet Layer
  All requirements of DoD led to the choice of a packet-switching network based on a connectionless internetwork layer
  This layer is called the internet layer, because it is the key player that holds the whole architecture together

## Slide 101: TCP/IP Reference Model
Internet Layer
  Job is to permit hosts to inject packets into any network and have them travel independently to the destination on a different network
  They may even arrive in a different order than they were sent
  It is the job of higher layers to rearrange them, if in-order delivery is desired

## Slide 102: TCP/IP Reference Model
Internet Layer
  Internet layer defines an official packet format and protocol called IP (Internet Protocol).
  The job of the internet layer is to deliver IP packets where they are supposed to go.
  Packet routing & avoiding congestion are the major issue here
  For these reasons, it is reasonable to say that the TCP/IP internet layer is similar in functionality to the OSI network layer

## Slide 103: TCP/IP Reference Model
Transport Layer
  designed to allow peer entities on the source and destination hosts to carry on a conversation
  Two end-to-end transport protocols
    TCP (Transmission Control Protocol)
    UDP (User Datagram Protocol)
  TCP
    Reliable connection-oriented protocol
    allows a byte stream originating on one machine to be delivered without error on any other machine in the internet.
    It fragments the incoming byte stream into discrete messages and passes each one on to the internet layer.

## Slide 104: TCP/IP Reference Model
Transport Layer
  TCP
    At the destination, the receiving TCP process reassembles the received messages into the output stream
    TCP also handles flow control to make sure a fast sender cannot swamp a slow receiver with more messages than it can handle

## Slide 105: TCP/IP Reference Model
Transport Layer
  UDP
    Unreliable connectionless protocol
    for applications that do not want TCP's sequencing or flow control and wish to provide their own
    also widely used for one-shot, client-server-type request-reply queries and
    applications in which prompt delivery is more important than accurate delivery, such as transmitting speech or video

## Slide 106: TCP/IP Reference Model
Application Layer
    TCP/IP model does not have session or presentation layers
    Because they are of little use to most applications
    contains all the higher-level protocols like
      virtual terminal (TELNET)
      file transfer (FTP)
      electronic mail (SMTP)
      Domain Name System (DNS)
      Network News Transfer Protocol (NNTP)
      Hyper Text Transfer Protocol (HTTP)

## Slide 107: TCP/IP Reference Model
Application Layer
    TELNET
      virtual terminal protocol allows a user on one machine to log onto a distant machine and work there
    FTP (File Transfer Protocol )
      provides a way to move data efficiently from one machine to another
    SMTP (Simple Mail Transfer Protocol)
      Electronic mail was originally just a kind of file transfer, but later a specialized protocol (SMTP) was developed for it

## Slide 108: TCP/IP Reference Model
Application Layer
    DNS (Domain Name System)
      for mapping host names onto their network addresses
    NNTP (Network News Transfer Protocol )
      protocol for moving USENET news articles around
      USENET (worldwide distributed Internet discussion system)
    HTTP (Hyper Text Transfer Protocol )
      protocol for fetching pages on the World Wide Web (WWW)

## Slide 109: Reference Models
Protocols and networks in the TCP/IP model initially.
ARPANET - Advanced Research Projects Agency Network
SATNET – Sustainable Agriculture Trainers Network

## Slide 110
Tutorial I
Comparison & critiques of OSI and TCP/IP Models